## Slide 1: Verilog Review

## Slide 7: FPGA Design Flow
Detailed (RTL)
Design
Design
Ideas
(Specifications)
Device
Programming
Timing
Simulation
Synthesis &
Implementation
Functional
Simulation
tpd=22.1ns
fmax=47.1MHz
FPGA
CPLD

## Slide 8: RTL Specification
Determine I/O signals or Ports
  Standard interface, protocol, custom interface
Partition design into functional blocks
  Datapath, Control logic, Memory, etc.
Determine block interfaces
Specify each block separately at RTL
  MUXs, counters, adders, registers etc.

## Slide 9: Detailed Design
  HDL (Hardware Description Language), e.g. Verilog, VHDL, SystemC
    Requires some experience, harder to debug
    Descriptive & portable
    Easy to modify
    Greater productivity
  Use vendor-supplied IP libraries to reduce design time
  Create & manage user-created libraries (circuits)

## Slide 10: Functional Simulation
Preparation for simulation
  Generate simulation patterns
    HDL testbench
  Functional simulation
  To verify the functionality of your design only
Simulation results
  Waveform display
  Text output
  Self-checking testbench
Challenge
  Sufficient & efficient test patterns

## Slide 11: HDL Synthesis
Synthesis = Translation + Optimization
  Translate HDL design files into gate-level netlist
  Optimize according to your design constraints
    Area constraints
    Timing constraints
    Power constraints
Main challenges
  Learn synthesizable coding style
  Use proper design partitioning for synthesis
  Specify reasonable design constraints
  Use HDL synthesis tools efficiently
assign z=a & b
a
b
z

## Slide 12
Logic Synthesis?

## Slide 13: The Verilog Language
Verilog is a parallel, hardware description language (HDL).
Originally a modeling language for a very efficient event-driven digital logic simulator
Later pushed into use as a specification language for logic synthesis
Virtually every chip (FPGA, ASIC, etc.) is designed in part using Verilog.
Combines structural and behavioral modeling styles

## Slide 16: The Verilog Language
Textual representation of Hardware constructs.
All statements are executed in parallel.
Code ordering is flexible.
  a=1;b=2;c=a+b → c==3
  c=a+b;a=1;b=2 → c==3
Execution of code is triggered by Events.
Sensitivity lists are used to define when a code section is executed
Different simulators may yield different results. Coding style is required

## Slide 17: Abstraction levels
• Three coding styles:
  Structural code (GTL (Gate Level), Netlist)
  RTL (Register Transfer Level)
  Behavioral (Testbench)
• DUT (Device Under Test)
  Represents Hardware
  Usually RTL or GTL
• Testbench
  Represents System
  Usually Behavioral
  Using higher order languages (“e”/SystemVerilog)

## Slide 49
Verilog for Sequential Circuits

## Slide 50
D-register in Verilog
Use of posedge/negedge makes an always block sequential (edge-triggered)
The <= describes a ‘non-blocking’ assignment.
Guideline : Always use <= for sequential logic. Why we will see later.
  module d_reg (input clk,
  input D,
  output reg Q) ;
  always @ (posedge clk)
  Q <= D;
  endmodule

## Slide 51
Problem: Verilog Code for the Circuit
  module d_circuit (input clk,
  input x,
  input y,
  output reg A) ;
  wire x_xor_y, D_A;
  assign x_xor_y = x^y;
  assign D_A = A^(x_xor_y);
  always @ (posedge clk)
  A <= D_A;
  endmodule
x
y
clk
A

## Slide 52
  module d_reg_rst (input clk,
  input reset,
  input D,
  output reg Q) ;
  always @ (posedge clk or negedge reset)
  begin
  if (reset == 0) Q<=0 // when reset
  else Q <=D // normal
  end
  endmodule
The following is incorrect syntax: always @ (reset or posedge clk)
If one signal in the sensitivity list uses posedge/negedge, then all signals must.
D-register with Asynchronous reset

## Slide 54
module nonblocking(in, clk, out);
input in, clk;
output out;
reg q1, q2, out;
always @ (posedge clk)
begin
q1 <= in;
q2 <= q1;
out <= q2;
end
endmodule
module blocking(in, clk, out);
input in, clk;
output out;
reg q1, q2, out;
always @ (posedge clk)
begin
q1 = in;
q2 = q1;
out = q2;
end
endmodule
Blocking vs non-Blocking

## Slide 56: Blocking & Non-Blocking Assignments – Example
Blocking
reg[7:0] A, B, C, D
always@(posedge clk)
begin
A = B + C;
B = A + D;
C = A + B;
end
Non-Blocking
reg[7:0] A, B, C, D
always@(posedge clk)
begin
A <= B + C;
B <= A + D;
C <= A + B;
end
initial begin
A = 8’h1; B = 8’h2; C = 8’h3; D = 8’h4; end

## Slide 57
Blocking assignments, "=" evaluate the RHS and update the LHS immediately before any further instructions are executed.
Non-Blocking assignments, "<=" evaluate the RHS and postpone updating LHS until the end of present simulation timestep.
Blocking vs non-Blocking : Summary

## Slide 58
Increment a multi-bit value on every clock
N-bit counter: counts from zero to 2N-1
Technically, an N-bit FSM with a looped state transition diagram
Easier to think about as register and adder components
Variations –
  Count down, count up/down
  BCD counter: 0 ➙ 9
Sequential Component: Counter

## Slide 59
  module counter(input clk,
  output reg [3:0] count) ;
  wire [3:0] D_count;
  assign D_count = count + 1;
  always @ (posedge clk)
  count <= D_count;
  endmodule
4-bit Counter

## Slide 60
  module counter(input clk,
  input enb,
  output reg [3:0] count);
  wire [3:0] D_count;
  assign D_count = enb ? count + 1 : count;
  always @ (posedge clk)
  count <= D_count;
  endmodule
4-bit Counter with enable

## Slide 61
4-bit Counter with enable and clear
  module counter(input clk, enb, clr,
  output reg [3:0] count) ;
  wire [3:0] D_count;
  assign D_count = clr ? 4’b0 : (enb ? count + 1 : count);
  always @ (posedge clk)
  count <= D_count;
  endmodule

## Slide 62
Problem: 4-bit Down Counter with enable and clear
  module counter(input clk, enb, clr,
  output reg [3:0] count) ;
  wire [3:0] D_count;
  assign D_count = clr ? 4’b1111 : (enb ? count - 1 : count);
  always @ (posedge clk)
  count <= D_count;
  endmodule
Cleared value should be 4’b1111

## Slide 63: Design of Clocked Sequential Circuits
Suppose we wish to design a circuit that detects a sequence of three or more consecutive 1’s in a string of bits coming through an input line (i.e., the input is a serial bit stream).
S0 : Reset State
S1: One 1 is detected
S2: Two 1s are detected
S3: Three 1s are detected -> Output = 1
the circuit stays in S3 as long as there are three
or more consecutive 1’s received

## Slide 64
State Table for Sequence Detector

## Slide 65
K-maps for Sequence Detector

## Slide 66
Final Circuit

## Slide 67
  // State Registers
  always @ (posedge clk)
  begin
  if (reset)
  begin
  A <= 0;
  B <= 0;
  end
  else
  begin
  A <= D_A;
  B <= D_B;
  end
  end
  endmodule
  module seq_det(input clk,
  input x,
  input reset,
  output detect) ;
  wire D_B, D_A;
  reg A, B;
  // Combinational Logic
  assign D_A = A & x | B & x;
  assign D_B = A & x | (~B & x);
  assign detect = A & B;
Verilog Structural Description

## Slide 68
module FSM_det(input clk, input, x, input reset, output detect);
reg [1:0] state, nextstate;
parameter S0 = 2'b00;
parameter S1 = 2'b01;
parameter S2 = 2'b10;
parameter S3 = 2’b11;
// State register
always @ (posedge clk)
if (reset) state <= S0;
else state <= nextstate;
// Next state logic
always @ (*)
case (state)
S0: if (x) nextstate = S1; else nextstate = S0;
S1: if (x) nextstate = S2; else nextstate = S0;
S2: if (x) nextstate = S3; else nextstate = S0;
S3: if (x) nextstate = S3; else nextstate = S0;
endcase
// Output logic
assign detect = (state == S3);
endmodule
Verilog FSM Abstraction

## Slide 69
Power of Verilog: Parameterized Static Elaboration

## Slide 70
Power of Verilog: Parameterized Static Elaboration

## Slide 71
Ripple Carry Adder

## Slide 72
Ripple Carry Adder : Using genvar

## Slide 73
Parameterized elaboration + genvar

## Slide 74
Parameterized elaboration + genvar

## Slide 75: Discrete-event Simulation
Basic idea: only do work when something changes
Centered around an event queue
  Contains events labeled with the simulated time at which they are to be executed
Basic simulation paradigm
  Execute every event for the current simulated time
  Doing this changes system state and may schedule events in the future
  When there are no events left at the current time instance, advance simulated time soonest event in the queue

## Slide 76
Reg vs Wire
Outputs of an always block must be declared as reg

## Slide 77
Reg vs Wire
Outputs of an assign statement must be declared as wire

## Slide 78
  module m3sample( input a, b, c, input [1:0] sel, output out );
  reg out;
  always @( * )
  begin
  case ( sel )
  2’d0 : out = a;
  2’d1 : out = b;
  2’d2 : out = c;
  default: out = 1’bx;
  endcase
  end
  endmodule
Dangers of Verilog #1
If sel = 3, mux will output the previous value. What have we created?

## Slide 79
module unknown
(input clk,
input d,
output reg q);
always @(*)
begin
if (clk)
q = d;
end
endmodule
What is inferred?

## Slide 80
  module prior1a (x, y, z, a, b, c, e, f, g);
  output x, y, z;
  input a, b, c, e, f, g;
  reg x, y, z;
  always @(a or b or c or e or f or g)
  begin
  {z,y,x} = 3’b0;
  if ((a==1) && (b==1)) z = 1;
  else if ((c==1) && (e==1)) y = 1;
  else if ((f==1) && (g==1)) x = 1;
  end
  endmodule
Dangers of Verilog #2

## Slide 81
Verilog allows us to do two things with the same piece of code:
Infer the physical structure of the logic to be created.
Simulate the behavior of the logic prior to building it.
We must write code to simultaneously satisfy two tools. In order of
importance...
Logic synthesizer - Our code must clearly infer the structure
(including errors!) we want from logic synthesis.
Logic simulator - Our code, when simulated, must exhibit the exact
behavior of the synthesized gates that are yet to be built.
Summary

## Slide 82
Don't keep hacking code till the simulator is happy... Its working
gates you want!
Well structured RTL code written with an eye towards logic
synthesis almost always simulates correctly. The synthesizer is way
pickier than the simulator. This is a big reason for our structure first approach.
Debugging is very difficult for Verilog. Don’t write code and “see if it works.” Test each “unknown” thing individually until you know what it does; then combine into larger entities. Divide and conquer!
Summary

## Slide 83
Verilog Coding Guidelines
Start with a Circuit Diagram. Don’t jump into coding without drawing the circuit diagram. Name all the input, output ports and internal wires. Always give meaningful names to ports, modules and wires. It increases readability and debuggability.
Use “assign” statements for simple combinational logic. Use combinational always blocks for complex combinational logic.
Clearly distinguish always blocks meant for combinational logic from those meant for sequential logic, do not mix combinational logic and sequential logic in the same always block
Only use blocking assignments (=) in combinational always blocks
Only use non-blocking assignments (<=) in sequential always blocks
Try to put as little logic in a sequential always block as possible. Keep it simple!
Write code which is aesthetically pleasing!

## Slide 84
Verilog for Verification

## Slide 92
  module counter_tb() ;
  reg clk, clr, enb;
  wire [3:0] count;
counter DUT ( .clk (clk), .clr (clr), .enb (enb), .count (count) );
  initial begin
  clk=0;
  forever #5 clk=~clk; //Clock Generator
  end
  initial begin
  #10 clr = 1'b1;
  #20 clr = 0;
  #10 enb=1;
  end
  endmodule
Counter Test Bench